## Slide 1: Motion Estimator
Karuna RC (915880893)
Premdeep Amudala (913773112)

## Slide 2: Requirements
16x16 Reference Block
31x31 Search Window
Search memory is two-read-ported memory
One memory per search
Grey-scale coded pixels (8 bits/block)
4096 reference blocks in a frame
Timing requirements:
  search speed at 15 frames per second
  Encoding is not in real time
  Clock: 260 MHz
Target Library: 90 nm CMOS library (standard max db)

## Slide 3: Design
Top Down Design
4096 blocks per 1/15 of a second
(31-15)x(31-15)=256 searches/block
16x16=256 add-accumulates per search
At 260 MHz At least 16 adders in parallel (4027/260=15.5)

## Slide 4: Elements in the Design
Processing Elements (PEs)
Controller
Comparator
Top Module

## Slide 5: Project Deliverables
Bug Free RTL
  Unit level testing
  Full-chip testing
System Verilog test bench for random stimulus based verification
  Verified for 1000 iterations
Synthesis
  Clock: 260MHz
  Input and Output Delays: Set at Zero
  Min Area, Min Power
Place and Route
  Chip Layout
  Chip Area
  Chip Power
Post-Layout Primetime
  Positive Slack on: Hold and Setup timings

## Slide 7: Processing Element: Bugs
Race Condition elimination due to temporary assignment to accumulator and registering this data to accumulate_out at clock
Computed absolute value, by using carry flag to identify the negative number

## Slide 8: PE Waveform

## Slide 9: Controller
Address generation logic
Bugs Fixed
  Address generation logic for search memory S2
  Compstart logic
  MotionY generation logic

## Slide 10: Controller: Waveform

## Slide 11: Comparator: Bugs
Compstart logic
One hot encoding based PE data selection

## Slide 12: Comparator: Waveform

## Slide 13: Full Chip Test bench: Waveform

## Slide 14: System Verilog Test Bench

## Slide 15: Design
Clock and Start
DUT
Checker
Memory Driver
Distortion and Vector Generator
Scoreboard
Memory
Results

## Slide 16: Test Flow
Memory Creation
Data Randomization
Distortions and Vector Generation
Spawn Threads
Assert Start
Memory Driver
Checker
Counter
Wait for Sync (all Threads to complete)
Finish

## Slide 17: Wave dump: Single seed

## Slide 18: Wave dump: Multiple seeds

## Slide 19: 1000 Seeds: Passed

## Slide 20: Enhancements
Performance
  Current enhancement of implementation of shift register to realize multiplication operations.
  Eliminating Race Conditions
Power Management
  Clock Gating of PE when the distortion reaches max value of FF
  Stopping the search when perfect match is found

## Slide 21: Physical Design

## Slide 22: Synthesis
Target Clock: 260 MHz: Period: 3.846 ns
Target Library: saed90_max.db
Input and Output Delay: 0 ns

## Slide 23: Place and Route
Target Library: saed90_max.db
Clock: 3.864ns

## Slide 24: Place and Route: Results
Chip Area: 3940 Sites

## Slide 25: Place and Route: Results: Cont’d
Chip Power: 66.8759 uW
Leakage: 8.9677 uW

## Slide 26: Post Layout: Timing reports
Hold Timing (Min): 1.33

## Slide 27: Post Layout: Timing reports
Setup Timing (Max): 0.33

## Slide 28: Project Deliverables: Achieved
Bug Free RTL - Done
  Unit level testing
  Full-chip testing
System Verilog test bench for random stimulus based verification - Done
  Verified for 1000 iterations
Synthesis - Done
  Clock: 260MHz (3.846ns) – MET: 0.81
  Input and Output Delays: Set at Zero
  Min Area, Min Power
Place and Route
  Chip Layout - Done
  Chip Area: Done: 3940 Sites
  Chip Power: Done: 66.8759 uW
Post-Layout Primetime
  Positive Slack on: Hold and Setup timings: MET (Hold: 1.33, Setup: 0.33)

## Slide 29: Thank you

## Slide 30: Block Diagram
Best Distortion and
Motion (x,y)
Motion Estimator
Processing Unit
(16 PEs)
Comparator
Controller
Data
Output
Clk / Start
Addr